## Slide 1: Digital Design and Computer Architecture
Course outcome 2

## Slide 2: PROJECT TITLE Design and Simulation of a Digital Access Card Verification System Using (2*1)Multiplexer

## Slide 3
Presented by
1.Sai Hitesh – 2620030269
2. Hyder – 2620030257
3. Radhika – 2620030258
4. Akshith - 2620030282

## Slide 4: Introduction
A Digital Access Card Verification System is a digital security system designed to control access to a protected area or system. Access is granted only when two conditions are satisfied:
The access card is valid.
The entered PIN is correct.
The system uses combinational logic and a 2:1 Multiplexer (MUX) to implement the required access-control logic.

## Slide 5: Objectives
The objective of this project is to design a digital access card verification system that grants access only when the card is valid and the PIN is correct.
Specific Objectives:
Card Verification – Checks whether the access card is valid.
PIN Verification – Checks whether the entered PIN is correct.
Access Control – Grants access only when both conditions are satisfied.
Security – Prevents unauthorized access.
Digital Implementation – Demonstrates combinational logic using a 2:1 multiplexer.

## Slide 6: Logic Design
Since, The system uses two inputs and one output:
Input A – Card Status:
0 = Invalid Card, 1 = Valid Card
Input B – PIN Verification:
0 = Incorrect PIN, 1 = Correct PIN
Output Y – Access:
0 = Access Denied, 1 = Access Granted
The required AND logic is implemented using a 2:1 Multiplexer

## Slide 7: 2:1 Multiplexer Logic
A 2:1 Multiplexer is used to implement the access-control logic.
The MUX connections are:
I₀ = 0 — Constant Logic 0
I₁ = B — PIN Verification
S = A — Card Status
Y = Access Output
When A = 0, the MUX selects I₀, which is 0. Therefore, access is denied.
When A = 1, the MUX selects I₁, which is B. Therefore, access depends on whether the PIN is correct.

## Slide 8: Working
The card reader first provides the Card Status (A).
If the card is invalid, A = 0. The MUX selects I₀ = 0, so access is denied.
If the card is valid, A = 1. The MUX selects I₁ = B.
If the PIN is incorrect, B = 0, so access remains denied.
If the PIN is correct, B = 1, so access is granted.

## Slide 9: Logisim Simulation
Place two input pins for Card Status (A) and PIN Verification (B).
Place a 2:1 Multiplexer.
Set Select Bits = 1 and Data Bits = 1.
Connect Constant 0 to I0.
Connect B (PIN Verification) to I1.
Connect A (Card Status) to the Select input (S).
Connect the MUX output to an output pin or LED.
Change the values of A and B and verify the truth table.

## Slide 10: Logisim Diagram

## Slide 11: Truth Table
A(Card Status) | B(Pin Verification) | Y(Access)
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 12: Boolean Expression
The required logic is:
Y = A · B
Where:
A = Card Status
B = PIN Verification
Y = Access
This represents AND logic because access is granted only when both conditions are true.

## Slide 13: Expected Result
Street light turns ON when it is dark and motion is detected.
Street light remains OFF during daylight.
Street light remains OFF when there is no motion.
The 2:1 MUX successfully controls the street light based on the sensor inputs.
The circuit is successfully simulated and verified in Logisim Evolution.
The system helps reduce unnecessary power consumption.

## Slide 14: THANK YOU